## Slide 1: Introduction to Programming(II) Week 06
李哲榮

## Slide 2: Computer System
Application Programs
Libraries
Operating System
Drivers
Memory
Manager
Scheduler
Execution Hardware (CPU)
Memory
Translation
System Interconnect
(Bus)
Controllers
Controllers
Main
Memory
I/O Devices
Networking
Instruction Set Architecture
Software
Hardware
Your code

## Slide 3: software
Application Programs
Libraries
Operating System
Drivers
Memory
Manager
Scheduler
Execution Hardware (CPU)
Memory
Translation
System Interconnect
(Bus)
Controllers
Controllers
Main
Memory
I/O Devices
Networking
Instruction Set Architecture
Software
Hardware

## Slide 4: Your Code
int input;
scanf(“%d”, &input);
if (input%2 == 0 )
printf(“%d is even\n”);
else
printf(“%d is odd\n”);
Functions in the standard C library

## Slide 5: Compiler and Linker
Your code will be compiled to an object file first

## Slide 6: Loader
Code can only be executed in the memory.
Loader is a system software that loads executable files from disk into memory (RAM) so that CPU can run the processes in RAM.
Memory
OS
Loader
Hard Disk
a.exe
Allocate a memory space
Open
Read file to RAM
Code
Data

## Slide 7: Bootloader
The bootloader loads OS when a computer is turned on.
https://neosmart.net/wiki/mbr-boot-process/
BIOS/UEFI
(ROM)
Bootloader
OS
Firmware on
motherboard
Software on disk
Notes: Unified Extensible Firmware Interface，縮寫UEFI

## Slide 8: What does OS do?
Resource abstraction:
  Ex: files (disk block), (input/output) device driver…
Resource management:
  Four major tasks
User Interface
Process (CPU)
Memory (RAM)
Files (Disks)
Input/output (Devices)

## Slide 9: Process Management
A single CPU can be used to run multiple processes (feel like) simultaneously.
Interrupt
Interrupt
Interrupt
Interrupt
Process A
Process switch
Process B
Process switch
Process A
Process switch
Process B
Process switch
0ms 50ms 150ms 250ms 350ms
Process B ready
Process A ready
Process B ready
Timeslice

## Slide 10: Memory Management
Handle the requests of malloc and free
Example:
  A = malloc(4)
  B = malloc(5)
  C = malloc(3)
  free(B)
https://www.ibm.com/developerworks/linux/library/l-memory/
D = malloc(4)
E = malloc(2)
free (C)
F = malloc(4)

## Slide 11: File System
Controls how data is stored in and retrieved from disks
Example (from wikipedia)
https://upload.wikimedia.org/wikipedia/commons/9/99/File_system_fragmentation.png

## Slide 12: IO Management
Handle the input/output of all devices
音效卡
網路卡
顯示卡

## Slide 13: Instruction set architecture
Application Programs
Libraries
Operating System
Drivers
Memory
Manager
Scheduler
Execution Hardware (CPU)
Memory
Translation
System Interconnect
(Bus)
Controllers
Controllers
Main
Memory
I/O Devices
Networking
Instruction Set Architecture
Software
Hardware

## Slide 14: What is an assembly code?
Consider the language translation from Chinese to English?
How is a program executed?
一個程式是如何被執行?
如何 是 一個 程式 被執行?
Analogy
C code
Assembly code
Machine code

## Slide 15: Why assembly?
C codes (or any high level programs) are very different from the machine code
#include <stdio.h>
int main(){
printf(“Hello World!”);
return 0; }
01101001001001001101010101010010100101010101010101101010101011101101010101110010101010101011010110...
Answers:
Human readable
One to one to machine code

## Slide 16: Hardware Level
Mother board (主機板)
Hard disk
(硬碟)
CPU (中央處理器)
Memory (記憶體)
ALU
(計算邏輯單元)
Registers
(暫存器)

## Slide 17: How is a program executed?
Mother board (主機板)
Hard disk
(硬碟)
CPU (中央處理器)
Memory (記憶體)
ALU
(計算邏輯單元)
Registers
(暫存器)
HelloWorld.c
Assembly code
Compiler
Assembler
Machine code
(Executable)
Machine code
(Executable)

## Slide 18: Machine code
A machine code is a sequence of “instructions”.
  The basic unit of machine codes is an “instruction”.
Example: a = b + c;
  mov [21] to r1
  mov [63] to r10
  add r1, r10, r5
  mov r5 to [D8]
1
2
1+2
3

## Slide 19: Discrimination
Name | Example | Meaning
Variable | a, b, c | The high level naming of memory space.
Value | 1, 2, 3 | The value stored in the memory space.
Memory address | [21],[63], [D8] | The address of memory where data are stored.
Register | r1, r5, r10 | Temporary storage of data inside CPU.

## Slide 20: Instruction format
Instructions are encoded in binary numbers.
Ex:
Op-code: Specifies which operation to execute
Operand: Gives more detailed information about the operation

## Slide 21: Instruction types
Data Transfer
  Copy data between CPU and memory/devices
  E.g., LOAD, STORE, device I/O,
Control
  Direct the execution of the program
  E.g., JUMP, BRANCH, JNE (conditional jump),
Arithmetic/Logic
  Use existing data values to compute a new value
  E.g., AND, OR, XOR, SHIFT, ROTATE, etc.

## Slide 22: Instruction execution
Uses logic circuits
Data transfer: load, store, …
  Logic circuit for registers (Ex: flip-flops)
Control: jump, jump-equal, …
  Change the value of program counter (PC)
  Comparison logic circuit
Arithmetic/Logic: add, and, shift, …
  Again, logic circuits

## Slide 23: User Mode/Kernel Mode
A computer usually has two modes for ISA:
  Kernel mode (OS): can run any instructions
  User mode (your code): can only run restricted instructions
User Mode
Kernel Mode
Interrupts, exceptions, system calls
Anytime OS wants

## Slide 24: Hardware
Application Programs
Libraries
Operating System
Drivers
Memory
Manager
Scheduler
Execution Hardware (CPU)
Memory
Translation
System Interconnect
(Bus)
Controllers
Controllers
Main
Memory
I/O Devices
Networking
Instruction Set Architecture
Software
Hardware

## Slide 25: Music analogy
Applications |  | Music, songs | 
Pro-grams | C code | Scores (樂譜) | Staff (五線譜)
 | Assembly code |  | Tab (指譜)
Computer |  | Instrument (樂器) | 
Death Waltz Synthesia
https://www.youtube.com/watch?v=O3Nc4iR7rGA
Like different kinds of instruments have different tabs;
different kinds of computers (CPUs) have different instruction sets.

## Slide 26: Who plays the music?
A computer is more like a music box, but the songs can be “programmed”.
Computer | Music box
1/0 | Touched /not
Electronic | Mechanic
Gates, circuits, … | Gears, screws,…
Program

## Slide 27: 紙卷鋼琴 Reproducing Piano Rolls
一排65-88個「木手指」置於普通鋼琴鍵盤上方，代替了鋼琴家的雙手。演奏器以打孔紙卷（打孔位置與鋼琴譜相符）記譜，用腳踏風箱鼓風作為動力，通過紙卷緩緩轉動，紙卷上的孔位與驅動機械連動相應的「木手指」擊琴鍵奏出音樂。此後又有設計者將外附的演奏器直接安裝於鋼琴內部，還可控制速度、力度、踏板等。
https://zh.wikipedia.org/wiki/%E8%87%AA%E5%8B%95%E6%BC%94%E5%A5%8F%E9%8B%BC%E7%90%B4

## Slide 28: AND gate
The AND Operation
Inputs
Output
0
AND 0
0
1
AND 0
0
0
AND 1
0
1
AND 1
1

## Slide 29: OR gate
The OR Operation
0
OR 0
0
1
OR 0
1
0
OR 1
1
1
OR 1
1
Inputs
Output

## Slide 30: XOR (eXclusive OR) gate
The OR Operation
0
XOR 0
0
1
XOR 0
1
0
XOR 1
1
1
XOR 1
0
Inputs
Output

## Slide 31: NOT gate
The NOT Operation
NOT 0
1
NOT 1
0
Input
Output

## Slide 32: Boolean operators
They are good for logic operations (bit operations), but how about arithmetic operations: +, -, *, /
Input |  | Output
A | B | A.and.B
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
Input |  | Output
A | B | A.or.B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
Input |  | Output
A | B | A.xor.B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Input | Output
A | Not A
0 | 1
1 | 0

## Slide 33: Boolean functions
Almost all binary operations of computers can be carried out by logic gates
Example: One bit adder
  Two inputs and two outputs (S: sum, C: carry out)
A: input 1
B: input 2
S: output 1
C: output 2

## Slide 34: Implementation of one bit adder
The truth table of an one-bit adder
Compare it to the truth table of Boolean function AND, OR, XOR, NOT
  S = A .XOR. B
  C = A .AND. B
A | B | S | C
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1

## Slide 35: 4 bit parallel adder

## Slide 36: CPU
Z
N
register
Memory
PC
IR
Controller
ALU
clock
Control
signal
Control
Datapath
Memory

## Slide 37: What can be a gate?
LEGO’s “mechanical gates”
  The AND gate

## Slide 38: Circuit gates
Can we flip the switches without hands?
A
B
AND gate
A
B
OR gate
A
NOT gate
A
B
A
B
XOR gate

## Slide 39: Electronic switch
The earliest one is the vacuum tube
  1884, Thomas Edison

## Slide 40: Transistor
The problems of vacuum tubes are slow, large, expensive, and easy to break.
Transistor can make it faster, smaller, and more robust.

## Slide 41: Transistors for logic gates
CMOS

## Slide 42: Integrated circuit (IC)
An electronic circuit consisted of transistors and other components in the thin substrate of semiconductor material.
Also known as IC, microchip, or chip.
Invented by Jack Kilby and Robert Noyce
  2000 Nobel Prize in Physics
VLSI: Very-Large-Scale IC
  More than million transistors

## Slide 43: Discrimination
Name | Example | Meaning
Boolean operations | AND, OR, XOR, NOT | Math (logic) concept
Logic gate | AND gate, OR gate, XOR gate | Physical device implementing Boolean operations
Bitwise operators | &, ¦, ^, ~, >>, << | High level language syntax to process bits

## Slide 44: Discrimination
Name | Example | Meaning
Boolean value | TRUE, FALSE | Math (logic) concept
Electronic signal | Ex: voltage high or low | 
Bit | 0,1 | Basic unit of data in computer system